## Slide 1
TEAM NAME:RTL REBELS
PROBELM STATEMENT NO: PS 06
PROBLEM STATEMENT TITLE: HARDWARE AES-128 SYMMETRIC
BLOCK CIPHER CORE WITH AXI-MM INTERFACE
PS CATEGORY : HARDWARE

## Slide 2
  .
Problem Statement
Real world problems :Secure data encryption is needed in FPGA/SOC systems
Why it matters : Protects sensitive data with fast hardware based AES
Current challenges :
Low LUT usage (<1500 )
High throughput ( 1 block)
No key/internal state leakage

## Slide 3
yOur Solution
  Project name : Secure & Resource optimized AES-128 FPGA Accelerator.
  One-line solution : A secure,high speed AES-128 hardware accelerator with AXI-MM interface and optimized FPGA resource usage.
  How it solves the problem :
  Uses dynamic resources sharing to achieve <1,500 LUTs.
  Targets 1AES block/10 clock cycles.
  Prevents key and intermediate state leakage through AXI-MM.

## Slide 4
Architectural
Block diagram

## Slide 5
Purpose of Blocks
AXI-MM Interface – Handles system data and control access.
AES Registers – Stores plaintext, key, control and final output.
AES Controller – Controls AES rounds and timing.
AES Datapath – Performs SubBytes, ShiftRows, MixColumns and AddRoundKey.
Key Expansion – Generates round keys on-the-fly.
Output Block – Provides the final 128-bit encrypted/decrypted data.
Architecture trade-off
Resource sharing – Lower LUT usage.
Pipeline folding – High throughput.
On-the-fly keys – less memory & better security.
Secure AXI-MM – Prevents key/state leakage.

## Slide 6
OUTPUTS AND RESULTS
AES-128 Encryption & Decryption – Securely encrypts & decrypts 128-bit data.
10-Cycle Processing – Targets one AES block within 10 clock cycles.
Low Resource Usage – Optimized to use less than 1,500 LUTs.
Secure AXI-MM Interface – Enables safe system-level data communication.
No Key Leakage – Internal keys and cipher states are kept protected.
FPGA Implementation – Designed for the Arty S7-50 FPGA board. �

## Slide 7
REFerence
FIPS 197 – Advanced Encryption Standard (AES) - https://csrc.nist.gov/#
Vivado Design Suite User Guide – https://share.google/3oxbU1rZyKmIiO8du
Advanced Encryption Standard – Morris.J.Dworkin et al.,- https://csrc.nist.gov/#
NIST-Advanced encryption standard - https://csrc.nist.gov/#
AMD-Vivado Design (UG900)- https://share.google/3oxbU1rZyKmIiO8du
ARM AMBA AXI-AXI Protocol Specification- https://developer.arm.com

## Slide 8
1.NO SLIDES SHOULD BE REUSED EXCEPT THE OUTPUT AND RESULT SLIDE (SLIDE 6)
NOTE: MAXIMUM OF 10 SLIDES (NOT MORE THAN THAT)
  TRY TO EXPLAIN THE CONTENT IN PROBLEM STATEMENT SLIDE 2 AND THE SOLUTION SLIDE 3 IN A NEAT BULLET POINTS AND TRY TO KEEP REST OF PRESENTATIONS WITH MINIMAL TEXT
3.KEEP YOUR EXPLANATION PRECISE AND EASY TO UNDERSTAND
4.IDEA SHOULD BE UNIQUE AND NOVEL.
5.YOU CAN ONLY USE PROVIDED TEMPLATE FOR MAKING THE PPT WITHOUT CHANGING THE IDEA DETAILS POINTERS (MENTIONED IN PREVIOUS SLIDES).
6.YOU NEED TO SAVE THE FILE IN PDF AND UPLOAD THE SAME ON GITHUB . WORD DOC OR ANY OTHER FORMAT WILL BE SUPPORTED
.
NOTE - YOU CAN DELETE THIS SLIDE (IMPORTANT POINTERS) WHEN YOU UPLOAD THE DETAILS OF YOUR IDEA ON GITHUB.